## Slide 1
COMPUTER ENGINEERING
MASTER’S DEGREE
PROTOTYPE PRESENTATION
CARLO PIO PACE
PRASHANT GAUTAM
GUARDIAN
Child & Pet Safety

## Slide 2
Preventable fatalities from vehicular heatstroke continue to occur globally, resulting from instances where children or pets are inadvertently left by themselves or where children gain unsupervised access to vehicles. To address this safety challenge, this paper proposes a Child and Pet Presence Detection (CPPD) system, covering its architecture, deployment, and performance assessment.
This system employs visual and acoustic sensors, to acquire data processed by a Raspberry Pi 3B+ to actively monitor the cabin environment immediately after vehicle closure. Upon detecting a living occupant, the system sends alerts to a designated caregiver.
ABSTRACT

## Slide 3
INTRODUCTION
The phenomenon of vehicular heatstroke, often referred to as "Hot Car Death“, is a critical safety issue that continues to claim the lives of vulnerable occupants, particularly young children and pets. When a vehicle is parked in direct sunlight, the interior temperature can rise rapidly due to the greenhouse effect.
Despite public awareness campaigns, these incidents frequently occur due to "Forgotten Baby Syndrome," a psychological phenomenon where a parent or a caregiver inadvertently leaves a quiet in the rear seat due to a disruption in routine, fatigue, or distraction. As modern vehicles become increasingly soundproof and tinted, manual detection by passersby becomes difficult, necessitating an automated technological solution, which could totally prevent those fatalities.

## Slide 4
Chart: Every 1000 Cases (Childs)
[1] C.-H. Choi, S. Hong, E. J. Jeong, and J. Han, “Infrared thermal imaging for embedded child presence detection system: Feasibility and performanceevaluation,” in Proceedings of the IEEE International Conference on ConsumerElectronics Asia (ICCE-Asia), Danang, Vietnam, 2024.
[2] C. -H. Choi, S. Hong, E. J. Jeong and J. Han, "Infrared Thermal Imaging for Embedded Child Presence Detection System: Feasibility and Performance Evaluation," 2024 IEEE International Conference on Consumer Electronics-Asia (ICCE-Asia), Danang, Vietnam, 2024
[3] J. Gillner, R. Taylor, and K. Thelen, “Radar-based breathing sensor for child presence detection in automotive applications,” in 2024 IEEE 67th International Midwest Symposium on Circuits and Systems (MWSCAS). IEEE, 2024,pp. 104–107.
STATE OF THE ART
[4] M. A. H. M. Nazri, S. A. B. C. Abdullah, A. Ahmad, F. H. K. Zaman, N. K.Mun, and M. F. M. Salleh, “In vehicle child presence detection using 60ghz radar,” in 2025 IEEE 8th International Conference on Electrical, Electronics,and System Engineering (ICEESE). IEEE, 2025, pp. 42–47.
[4] Y. Su, F. Zhang, K. Niu, T. Wang, B. Jin, Z. Wang, Y. Jiang, D. Zhang,L. Qiu, and J. Xiong, “Embracing distributed acoustic sensing in car cabin forchildren presence detection,” Proceedings of the ACM on Interactive, Mobile,Wearable and Ubiquitous Technologies, vol. 8, no. 1, Mar. 2024.

## Slide 5
THE SYSTEM USE A COMBINATION OF SENSORS AND AI MODELS TO DETECT THE PRESENCE OF A CHILD OR PET , UNACOMPAINED INSIDE A CAR.
IN SUCH CASE SEND AN ALERT TO THE USER.
SYSTEM FUNCTIONALITIES

## Slide 6
BRAIN MODULE
Coordinates eye and ear, and classification modules, process their output, evaluate the state and if necessary trigger the communications module.
EYE MODULE
Acquires images from the camera,
pre-process them, then send the result
to the image classification module.
EAR MODULE
Acquire the sound, and the pre-process it, provide the output to the audio classification module
PROTOTYPE ARCHITECTURE
COMMUNICATIONS MODULE
Once triggered, sends the alert to a designated caregiver, leveraging the Telegram APIs.
IMAGE CLASSIFICATION MODULE
Detects the cabin occupants and sends
the result to the brain module.
AUDIO CLASSIFICATION MODULE
Classify the audio and sends the result to the brain module.

## Slide 7
IMAGE BASED DETECTION MODEL
DETECTS :
  ADULTS
  CHILDS
  PETS
PROTOTYPE ARCHITECTURE
SOUND BASED DETECTION MODEL
DETECTS :
  ADULTS SOUNDS (SPEAKING)
  CHILDS SOUNDS
  PET SOUNDS (BARKING)
  NOISE
  SILENCE

## Slide 8
STATE OF THE ART
[3] Sapkota, R., Cheppally, R. H., Sharda, A., & Karkee, M. (2026). YOLO26: Key Architectural Enhancements and Performance Benchmarking for Real-Time Object Detection. arXiv:2509.25164.
[4] Cao, J., Peng, B., Gao, M., Hao, H., Li, X. and Mou, H. (2025), Object Detection Based on CNN and Vision-Transformer: A Survey. IET Comput. Vis, 19: e70028. https://doi.org/10.1049/cvi2.70028
[5] Ali, M. L., & Zhang, Z. (2024). The YOLO Framework: A Comprehensive Review. Computers, 13(12), 336. https://doi.org/10.3390/computers13120336
[1] Van Thanh, Hoang, et al. "An Efficient Object Detection Model Based on NanoDet." 2025 International Workshop on Intelligent Systems (IWIS). IEEE, 2025
[2] Yerulan, Turganbek, and Duisebekov Zhasdauren. "COMPARATIVE STUDY OF LIGHTWEIGHT OBJECT DETECTION MODELS FOR MOBILE PEDESTRIAN DETECTION." Universum: технические науки 10.5 (134) (2025): 4-8.

## Slide 9
STATE OF THE ART
[8] Valliappan, N. Harihara, Sagar Dhanraj Pande, and Surendra Reddy Vinta. "Enhancing gun detection with transfer learning and YAMNet audio classification." IEEE Access 12 (2024): 58940-58949.
[9] Liu, LiFeng, et al. "YAMNet-based transfer learning for compact noise classification in urban and wireless systems." EURASIP Journal on Wireless Communications and Networking 2025.1 (2025): 74.
[10] Sakaki, Haruka, et al. "Comparative Evaluation of CNN, VGG16, Conformer, and YAMNet Models for Skateboard Riding Sound Detection." 2025 International Symposium on Multimedia and Communications Technology (ISMAC). IEEE, 2025.
[6] Gourisaria, Mahendra Kumar, et al. "Comparative analysis of audio classification with MFCC and STFT features using machine learning techniques." Discover Internet of Things 4.1 (2024): 1.
[7] Podda, Alessandro Sebastian, et al. "CARgram: CNN-based accident recognition from road sounds through intensity-projected spectrogram analysis." Digital Signal Processing 147 (2024): 104431.

## Slide 10
AI MODELS : COMPARISON
IMAGE BASED DETECTION MODELS
MODEL | PARAMETERS [millions] | RESOLUTION | mAP50
picoDET | 2.15 | 416 | 0.86
nanoDET | 6.1 | 480 | 0.89
Yolo v5 NU | 2.6 | 640 | 0.924
Yolo v11 N | 2.6 | 640 | 0.917
Yolo v12 N | 2.6 | 640 | 0.922
Yolo v26 N | 2.4 | 480 | 0.905
Yolo v26 N | 2.4 | 640 | 0.928
Yolo v26 S | 9.5 | 640 | 0.947

## Slide 11
AI MODELS : COMPARISON
MODEL | PARAMETERS [millions] | Accuracy
SPECTROGRAM+CNN | 0.024 | 0.72
MFCC + SVM | 0.05 | 0.86
YAMNet+FFN | 0.66 | 0.88
SOUND BASED DETECTION MODEL

## Slide 12
HARDWARE SETUP

## Slide 13
RASPBERRY PI 3 MODEL B+
Processor: 1.4GHz 64-bit quad-core Broadcom BCM2837B0, Cortex-A53 (ARMv8) SoC.
Memory: 1GB LPDDR2 SDRAM.
Wireless Connectivity: Dual-band 2.4GHz and 5GHz IEEE 802.11.b/g/n/ac wireless LAN, Bluetooth 4.2/BLE.
GPIO: Extended 40-pin GPIO header.
Camera Support: CSI camera port for connecting a Raspberry Pi camera.
Power Input: 5V/2.5A DC power input.
Sensor: Sony IMX219, 8-megapixel sensor.
Capabilities:
  High-definition video recording: 1080p30, 720p60, VGA90 video modes.
  Still image capture.
Connection: Attaches via a 15cm ribbon cable to the CSI port on the Raspberry Pi.
Software Support: Numerous third-party libraries are available, including the Picamera Python library.
RASPBERRY PI CAMERA MODULE (V2.1)
HARDWARE SETUP

## Slide 14
C MEDIA ELECTRONICS USB SOUND DEVICE
Processor : insert specs.
USB Version : 1.1
Channels : 1.
Sample Rate : 44100 Hz.
Audio Format : PCM.
Bit Resolution : 16 bits.
HARDWARE SETUP

## Slide 15
OpenCV
Raspberry Pi 3 +
Raspberry Pi
Camera
Image
CAMERA INTEGRATION

## Slide 16
EYE MODULE
Frame
pre-processing Pipeline
Acquired frame
Processed
frame
Bounding Boxes
&
Labels
Image with detections

## Slide 17
Python
Sounddevice
MICROPHONE INTEGRATION
Microphone
Raw audio signal

## Slide 18
EAR MODULE
Audio
pre-processing Pipeline
Classifications
Audio
Embeddings
Processed
Audio
Raw
Audio
YAMNet
FFN

## Slide 19
COMMUNICATIONS MODULE
LEVERAGES TELEGRAM APIs TO SEND 2 TYPES OF ALERT :
  Visual Alert :
    when a vulnerable occupant is detected through image, it sends a message and the image containing the ROI.
  Sound Alert :
    When the occupant is detected through sound, it send a message and the audio containing the sound.

## Slide 20
DECISION LOGIC

## Slide 21
GUARDIAN : FIRST VERSION
SEQUENTIAL APPROACH :
  Acquire image
  Record audio
  Inference on image
  Inference on audio
  Compute output, and if
  needeed send the alert
CHARACTERISICS :
  Sequential approach
  Yolo 26 Nano 480 (Image Model)
  Inference on audio (Spectrogram on 5s audio)
PROBLEMS:
  Recording the audio was the main bottleneck (waiting 5 seconds)
  Output each 6 seconds on average

## Slide 22
INFERENCE TIME
COMPARISON

## Slide 23
INFERENCE TIME
COMPARISON
IMAGE MODELS
SOUND MODELS
Chart: Yolo v26
| Nano 480 | Nano 640 | Small 640
Serie 1 | 0.8048 | 1.4343 | 5.2359
Chart: Time[s]
| MFCC+SVM | CNN+Spectrogram | YAMNet
Serie 1 | 0.0175 | 0.0206 | 0.02

## Slide 24
OPTIMIZATION

## Slide 25
IMPROVEMENTS:
  Parallel approach (Exploiting Multiprocessing library and IPC)
  Audio model improvements, dataset optimizations, needs shorter audio (3 seconds)
  Switch to YOLO 26 Nano 640
OPTIMIZATION

## Slide 26
EYE PROCESS : STANDALONE PROCESS , INITIALIZE CAMERA, ACQUIRE THE IMAGE, PROCESS IT, MAKE INFERENCE , PROVIDE DETECTIONS AS OUTPUT
EAR PROCESS : STANDALONE PROCESS , INITIALIZE MICROPHONE, RECORD AN AUDIO, PROCESS IT, MAKE INFERENCE , PROVIDE DETECTIONS AS OUTPUT
BRAIN PROCESS : MAIN PROCESS, STARTS EYE AND EAR PROCESS, WAITS THEIR OUTPUT, EVALUTE THE STATE, SEND ALERT MESSAGES
GUARDIAN : OPTIMIZED VERSION

## Slide 27
GUARDIAN : OPTIMIZED VERSION
480 X 480
640 X 640

## Slide 28
LIVE DEMO

## Slide 29
POSSIBLE SCENARIOS :
  ADULT IN FOV (FIELD OF VIEW)
  ADULT + BABY IN FOV
  ADULT + PET IN FOV
  BABY ALONE IN FOV
  DOG ALONE IN FOV
  ADULT IN FOV + CHILD CRYING
  CHILD CRYING
  PET SOUNDS
  ADULT SOUNDS
  SILENCE
IMAGES READ FROM FILE
EAR MODULE IN STANDY (NO SOUND)
LIVE IMAGES
NOTHING IN FOV
EAR MODULE ACTIVE
LIVE DEMO

## Slide 30
PERFORMANCES

## Slide 31
PERFORMANCES
METRICS USED
Mean Cycle Time [s]
Average time elapsed from data acquisition to system output.
Jitter [s]
Standard deviation of, indicating timing consistency
Throughput [dps/dpm]
Frequency of decision-making (system decisions per second and decision per minute)
CPU Load [%]
Represents the computational demand of the system’s processes relative to the Raspberry Pi’s processing capacity
RAM Usage [Mb]
Indicates the RAM memory usage of system’s processes
CPU Temperature [°C]
Monitors thermal stability to ensure the system avoids frequency throttling during extended operation

## Slide 32
PERFORMANCES
Average Metric | V1 (Sequential) | V2(Optimized)
Mean Cycle Time [s] | 5.9875 ± 0.0084 | 3.3259 ± 0.003
Jitter [s] | 0.037 | 0.199
Throughput [dps] | 0.167 ± 0.0002 | 0.3007 ± 0.0003
Throughput [dpm] | 10.02 ± 0.01 | 18.04 ± 0.002
CPU Load [%] | 16 ± 6.77 | 24.31 ± 4.53
RAM Usage [Mb] | 379.75 ± 0.3294 | 396.8125 ± 2.5408
CPU Temperature [°C] | 55 ± 0.2505 | 57.7647 ± 1.7267
CI 99% (EXCLUDED JITTER)

## Slide 33
PERFORMANCES
Yolo V26 (Converted to TFLite Model)
INFERENCE TIME : [1.4287,1,44] [s] (CI 99%)
Size : Nano
Resolution : 640 X 640
Recall : 0.893 %
mAP50 : 0.923 %
mAP50-95 : 0.675 %

## Slide 34
PERFORMANCES
YAMNet+FFN (Converted to TFLite Model)
INFERENCE TIME : [0.0187,0,0021] [s] (CI 99%)
Accuracy : 0.88 %

## Slide 35
CONCLUSION
A multimodal Child and Pet Presence Detection (CPPD) prototype was successfully developed and validated to prevent vehicular heatstroke caused by Forgotten Baby Syndrome.
The system combines vision and audio processing on a Raspberry Pi 3B+ to overcome limitations of camera-only solutions (e.g., low light, occlusion, blind spots).
Optimizing the architecture from sequential to parallel processing reduced detection time from 6s to 3.32s, enhancing real-time responsiveness.
Decision-level fusion allows the system to distinguish between safe (adult present) and critical (unattended child/pet) scenarios and send immediate alerts.
Results confirm that a low-cost edge-computing solution can deliver reasonable accuracy and fast response, making it a practical automotive safety enhancement.

## Slide 36
THANKS FOR YOUR ATTENTION